RS232 operation instructor

PROPERTY RIGHTS RESERVED

### 1、Hardware Environment & Connections

1） For RS232 operation, the devices are as follows:

PC, RS232 Cable, DVR

If there is only laptop computer, USB to RS232 cable is required.

2） Connection Mode is as follows:

PC --- RS232 cable --- DVR

DVR to laptop computer                     DVR to pc

### 2、RS232 operation

1） Run NOCM in your computer, the com set is as follows:

2） Get the serial port information from DVR(Debug state)

A、Restart the DVR ，press“ * ”key of your PC keyboard 3 times (upper right on number pad) when the words Hit any key to stop autoboot are on screen.

B、Now you can enter TFTP menu, and will see DVR> in the screen

C、Type setenv appauto 0

setenv dh_keyboard 0

save

then you will get the RS232 information from the DVR

E、Restart the DVR or type bootd to startup the DVR

Illustration below is the operation interface.

F、When you open the RS232 information, the DVR will not startup itself, and will stop at    #PHY: 0:00 – Link is Up – 100/Full

#

You need to type ii to start the DVR

E、All the information can be found in the ncom log file

3）Close the serial port information printing of the DVR

We need to set DVR to this state before it is sent to customer

For most users they do not need to open the serial port printing of the DVR, so we must close before the DVR is sent to the users

The operation is the same

A、Restart the DVR ，Click 3 *  to enter setup interface, and will see DVR> in the screen

C、Type setenv appauto 1

setenv dh_keyboard 1

save

D、Restart the DVR or type booted to startup the DVR

Illustration below is the upgrade interface.

4）Clear config of the DVR

Some time customer may need to clear the config of the DVR (when you can not set the right config through the DVR menu)

open the RS232 information and stop at

#PHY: 0:00 – Link is Up – 100/Full

#

- Type cd /mnt/mtd/Config to enter the Config directory

type ls to list the files

type rm * to clear the config

type ls to list the files again

Note: The DVR will auto popup some information, just ignore it and input what you want to input

- Type ii to start the DVR