TFTP upgrade instructor

PROPERTY RIGHTS RESERVED

### 1、Hardware Environment & Connections

1） For RS232 operation, the devices are as follows:

PC, RS232 Cable, DVR, network cable

If there is only laptop computer, USB to RS232 cable is required.

2） Connection Mode is as follows:

PC --- RS232 cable --- DVR

PC--- through network --- DVR

DVR to laptop computer                     DVR to pc

### 2、TFTP Upgrade

1）Unzip the upgrade software to you PC

make sure there are this two files

armboot-x.bin.img

armboot.bin.img

armboot64.bin.img

update.img

2） Run TFTP server

A、Run TFTP server: TFTPServer_En.exe

B、Set the upgrade route in the TFTP server, please see the picture below

3） Run NOCM in your computer, the com set is as follows:

4） See RS232 parameter

A、Restart the DVR ，press“ * ”key of your PC keyboard 3 times (upper right on number pad) when the words Hit any key to stop autoboot are on screen.

B、Now you can enter TFTP menu, and will see s3c2510 # in the screen

C、Type “printenv” to show some information of the DVR

5） TFTP upgrade

A、 Type  “setenv serverip  “ ip address of the PC” to set the TFTP server ip

Type  “setenv ipaddr “ip address of the DVR” to set the DVR ip

Type “save” to save

- Restart the DVR ，press * to Enter the TFTP menu again ,

Type “run da” to upgrade armboot software, it will take about 20-30 seconds

- Wait until you see s3c2510 # in the screen again

Attention: Never do anything that will stop the upgrade armboot

Such as : power off the DVR , disconnect the network , disconnect the RS232 cable

- Restart the DVR ，press * to Enter the TFTP menu again

Type “mac mac address of the DVR” to set mac address

Type  “sip ip address of the PC” to set the TFTP server ip

Type  “lip ip address of the DVR” to set the DVR ip

Type “save” to save

D、Restart the DVR ，press * to Enter the TFTP menu again

Type “run up” to begin upgrade

E、Wait until you see s3c2510 # in the screen again

F、Restart the DVR, and that’s all

6）Upgrade Failure

1、To check if the RS232 serial port and serial cable is OK

2、To check if the network connection is OK

3、To check if the mac address of the DVR is right

4、To check if the upgrade software is in the right folder and with right name

5、To check if the NCOM and TFTP software is running

6、Upgrade by TFTP upgrade again

7、After several times attempt, if there is still have problems, please contact with our technical engineers.

## More Details

If you still have any problems about these functions, please contact with our engineers.